# HTI Filtration Inc.

SYSTEM SPECIFICATION SHEET

HS410-C1-B4H-D

Model # 810-003

Systems Description: The 810-003 filtration system is designed to remove moisture, sludge, varnish and hard particulate from hydraulic fluids to 500 SUS viscosity used or directional and proportional valves. The filtration system features a rugged, floor mount stand and comes complete with a dedicated pump, motor and connection fittings. The heart of the system is the unique, high capacity 400 Series Hydra-Supreme filtration element that has proven itself capable of maintaining new oil quality over extended periods of time thus greatly extending the time between periodic fluid replacement, maintaining system accuracy and reducing internal wear.

Physical Data:

Height: 42"   (107 cm)

Width:  13"   (33 cm)

Depth:  18"   (46 cm)

Weight: 90 lb. (41 kg)

Material:

Stand  - Galvanized steel with powdercoat

Canister - Electroless Nickel coated mild steel

Drain valve - Brass

Fittings - Stainless steel

Performance Data:

Pump type: Rotary ring gear, internal relief

Flow:  3.0 GPM  (oil: 350 SUS @ 100°F)

11.5 l/min (oil: 650 Cs @ 40°C)

Oil Cleanliness - ISO 4406 16-14-12 typical

Electrical Specifications:

Motor - 1/2 HP TEFC /.37 kW 50/60 Hz Metric

12 Ft. , 16/4 SEOOW cord

Connection Data:

Oil inlet - 3/4" male 37' JIC

Oil Outlet - 1/2" male 37' JIC

810-003system spec 061812