# HTI Filtration Inc.

SYSTEM SPECIFICATION SHEET

HS410-C1-B6Q-A

Model # 810-004

Systems Description: The HS410-C1-B6Q-A filtration system, is designed to remove moisture, sludge and hard particulate from heavy duty gear lubricants up to 3500 SUS viscosity. The filtration system features a rugged, floor mount stand and comes complete with all required hoses, valves and connection fittings. The heart of the system is the unique, high capacity 400 Series Hydra-Supreme filtration element that has proven itself capable of maintaining new oil quality over extended periods of time thus greatly extending the time between periodic lube replacement and reducing internal wear in the gear box. This system has proven applications on lauter tun, mash tun and cooker drives boxes in brewing operations as well as other applications where water and high shear characteristics create premature wear on the drive gears.

Physical Data:

Height: 42"   (107 cm)

Width:  13"   (33 cm)

Depth:  18"   (46 cm)

Weight: 90 lb. (41 kg)

Material:

Stand and Canister -EN coated mild steel

Valve and drain plug - Brass

Performance Data:

Pump type: Rotary ring gear, external relief

Flow:  .5 GPM  (oil: 3500 SUS @ 100°F)

1.9 l/min (oil: 650 Cs @ 40°C)

Oil Cleanliness - ISO 4406 16-14-12 typical

Beta3:75

Electrical Specifications:

Motor – .37Kw/.5 HP 50/60 HZ 3 Phase

12 Ft. Connecting Cable

Connection Data:

Oil inlet - 3/4" male 370 JIC

Oil Outlet - 1/2" male 370JIC

810-004 system spec wb