HTI Filtration Inc.

SYSTEM SPECIFICATION SHEET

HS410-CH-B6L-UNP

Models # 810-011

Systems Description: The HS410-CV-B6L-UNP filtration system is designed to remove moisture, sludge and hard particulate from gear lubricants used in Sequa B-5 body makers.  The Model 810-009 models are bolt-on replacements for the Kaydon filters used on systems with cart mounted heat exchangers where the heat transfer tubes are horizontally mounted. The heart of these systems is the unique high capacity B6L Series Hydra-Supreme filtration element that has proven itself capable of maintaining new oil quality over extended periods of time. Using this filtration system eliminates the need for periodic gearbox lube replacement due to increasing water and metal content, reduces tear-off rates by keeping the lee jets open, and improves component life by reducing wear. Bodymakers with over 100 PSI normal operating pressure on the heat exchangers will need to add pressure reducing valve kit # 460-013 in order to maintain a safe operating environment.

Physical Data:

Height: 36"     (92 cm)

Width:  13"     (33 cm)

Depth:  13"     (33 cm)

Weight: 60 LB. (41 kg)

Material:

Stand and Canister - EN coated mild steel

Flow Control Valve - Brass, 300 PSI

Flow Meter - Aluminum body, acrylic scale tube

Performance Data:

Flow: 1.5 GPM  (oil: 750 SUS @ 100°F)

5.7 l/min (oil: 108 Cs @ 37.7°C)

Connection Data:

Oil inlet - 3/4" male 37O JIC

Outlet - 3/4" male 37O JIC

Options:

Pressure Reducing Valve Kit  460-013

810-011, -012 system specification wb  010301