OPERATORS MANUAL

HYDRA-SUPREME FLUID SCRUBBING SYSTEM

HS410-C2-B6L-C-SPEC.SCM

MODEL 810-013 and 810-027

SEQUA CANFORMING EQUIPMENT APPLICATION

INTRODUCTION:

Hydra-Supreme fluid scrubbing systems are high performance industrial filters designed to remove particulate, oxidized oil and water from hydraulic and lubricating fluid systems.  This particular model, HS410-C2-B6L-C-SPEC.SCM is specifically designed for cleaning the lubricating oil in Sequa Model B-6, high speed, can making systems. Manufactured from durable, corrosion resistant materials, it is designed for constant, uninterrupted use without immediate supervision.  This system will assure the required high degree of fluid purity with an absolute minimum of maintenance and service requirements.

SYSTEM OPERATION:

The Hydra-Supreme fluid scrubbing system utilizes a patented cellulose element to clean the working fluid of accumulated debris. The cleaning process utilizes three interlocking processes to remove solid particulate, varnish and water from the oil.  By combining barrier filtration, chromatographic separation and absorption all three of the listed contaminants can be removed from the oil simultaneously and efficiently.  As the filter traps the contaminants it builds up resistance and the pressure rises. At 60-65 PSI the pressure switch contacts activate the warning light signaling the need for filter replacement.

The proper function of the filter depends on the correct placement of the inlet and return lines, the correct flow volume, delivery and pressure.  The transfer lines should pull fluid from the reservoir and return it to a location at least 24" away to prevent recirculating the same oil over and over. A drawing is provided by Sequa which shows he proper inlet and return line locations.  The rotary ring gear pump provides extremely smooth fluid delivery to prevent pulsation’s that can from dislodge debris from the filter element.  Combining smooth delivery with the proper flow volume assures high trapping efficiency and long

element life.  Under normal conditions your Hydra-Supreme element should last 2-4 months before requiring changeout.  The filtration efficiency begins to drop off sharply as the pressure rises above 60 PSI and the filter element will begin shedding debris back into the oil above 65 PSI.

SYSTEM PRESSURE:

Pressure readings will vary with the viscosity of the oil used, the operating temperature of the reservoir and the amount of debris absorbed by the filter.

Typical start-up pressures using 750 SUS oil at 1000 F is 12-18 PSI.

Typical change out point is 60-70 PSI or a 50-PSI increase in original operating pressure but not to exceed 75 PSI.

Pump output pressure is controlled by an internal relief valve that is factory set to open at 70 PSI and go into complete bypass at 90-PSI maximum.  Do not change this setting. Removing the acorn nut can result in an intake air leak that will require a new gasket to correct.

Under no circumstance should your unit ever exceed 90 PSI. Should this occur shut down the system and contact the Hydra-Tech Technical Service Department at (714) 799-7757 assistance.

SYSTEM LOCATION:

Although the Hydra-Supreme system uses a self priming pump it is important to keep the filter as close to the reservoir as possible. The suction line should be less than 8' long and use ¾” fittings throughout the delivery line.

Set the filtration system on a solid, level surface.  Allow a minimum of 24" of frontal clearance for service access.  Filter system should be kept free of moisture and under 140o F.

PLUMBING:

The suction port utilizes a 3/4" inlet with NPT hose fittings.  A maximum hose length of 8' is recommended as is the use of sealing caulk or tape on all threaded fittings.

The return port utilizes a 3/4" line with NPT hose fittings. Sealing caulk or tape is also recommended on all threaded fittings.

Ball valves can be installed on both connections for easy shut-off during installation, adjustment or service.

ELECTRICAL:

The filter power system should be independent of the machine power, as the oil scrubbing system should run continuously for efficient contaminant control.

The motor for 810-013 systems is 115/230VAC 50Hz 1 Phase

The motor for 810-027 systems is 115/230 VAC 60Hz 1 Phase

The warning light operates on 115-230 volt, 50 / 60 Hz.

The pressure switch operates with either 115 VAC or 12-36 VDC power.

INITIAL START-UP PROCEDURE

Upon completion of the electrical and hydraulic connections the Hydra-Supreme is ready for start-up. The pressure relief valve is factory set for a maximum operating pressure of 90 PSI.  If your unit exceeds this level during any phase of operation it should be turned off immediately and Hydra-Tech should be contacted for instructions.

Open all valves on the inlet and return lines.

Crack open the bleed valve on the top of the canister.

Turn on the pump.

Close the bleed valve as oil starts to flow from it.

Check for fluid leaks before leaving the area.

Field Adjustment of Pressure Switches

The pressure switch can be field adjusted to activate the strobe light at higher or lower pressures than the 60-65 PSI setting established at the factory.

NOTE: Do not attempt to reduce or increase the operating pressure by adjusting the pressure relief valve. This safety devise has been set and locked into place at the

factory.

Refer to the Diaphragm Pressure Switch Drawing in the Appendix for electrical fitting orientation

To adjust the pressure switch connect a multi-meter to terminals 1 (bottom spade fitting) and 2 (left-hand, N/C spade fitting)

- Turn filter system on and vent any accumulated air

through the bleed cock on the canister lid.

2.      As soon as fluid flows from bleed cock, close and secure it.

- Allow filter system to run until it is up to operating temperature. Note the

operating pressure of the filter.

4.	Slowly close the outlet line ball valve until the system pressure is where you want the alarm light to activate.

5.        Turn the switch adjustment screw clockwise (to the right) until warning light                         contact closes. If the light is set too high turn the screw outwards (CCW) until                       the contacts break.

6.	Open the ball valve to relieve the pressure build-up, replace switch cover and record changes for future reference.

810-013  manual

11-01-00