# HTI Filtration inc.

SYSTEM SPECIFICATION SHEET

HS210-ENCSS-B4L-A

System # 810-020

System Description: Hydra Supreme filtration systems are designed to remove moisture and debris from hydraulic and lubricating oil circuits. The ENC models are installed in stainless steel, water resistant enclosures for use in food preparation areas or harsh environment applications. This system utilizes the unique, high efficiency Hydra Supreme series filter to remove both hard and soft particulate, as well as free and emulsified water from hydrocarbon based oils. The HS210 model is designed for  gear drive, lubricating and hydraulic fluids ranging from 350 to 1000 SUS (at 100 F). Each system comes complete with oil lines and quick disconnect fittings, watertight electrical connector, TEFC motor, pump with internal relief valve and integrated electrical connector panel. Cabinets can be ordered mounted on casters for ease of movement for cleaning or access.

Physical Data:

Enclosure type: NEMA 4X construction

Enclosure Height: 30"  (76 cm)

Width:	24   (61 cm)

Depth:	12"  (31 cm)

Legs: 12” (31 cm), with casters  16” (41cm)

Weight: 220 lb.  (100 kg)

Material:

Cabinet:304 Stainless steel, line grain finish

Fluid and electrical fittings: 316 stainless steel

Optional Casters: 304 SS body and frame

neoprene wheels, Delrin bearings

Performance Data:

Pump type: Rotary ring gear, internal relief

Flow: .5 GPM  (oil: 750 SUS @ 100°F)

1.9 l/min (oil: 108 Cs @ 37.7C)

Water Retention Capacity:  .75 liter typical

Electrical Specifications:

Motor - 1/3 HP TEFC  50/60 Hz 1 Ph

Heater blanket - 400 Watts, temp. controlled

Timer relay- 10 AMP  36-3600 sec. adjustable

Connection Data:

Oil inlet - ½” male 37o JIC

Oil outlet -3/8” male 37o JIC

Electrical - NEMA L5-20 watertight on 5’ SOW cord

Electrical Connectors - DIN 025

810-020 system specification wb 2-20-99