| TROUBLESHOOTING GUIDE HTI FILTRATION SYSTEM HS210-ENCSS-B4LM-A KRONES MODEL 810-036A When using this guide please remember that all pressure readings are to be taken with the system at normal operating temperatures. |
| --- |
| SYMPTOM | CAUSE | CORRECTIVE ACTION |
| ERRATIC FLOW RATE, BUBBLES IN OIL STREAM | AIR LEAK IN INLET FITTING | CHECK FITTINGS FOR TIGHTNESS AND INTEGRITY, |
|  | CUT OR PINCHED FEED HOSE | VISUALLY CHECK INLET HOSE FOR DEFECTS |
|  | LEAKING VACUUM GAUGE | REPLACE GAUGE WITH BOLT,IF LEAK DISAPPEARS REPLACE GAUGE |
| EXCESSIVE VACUUM (ABOVE 20") | INLET PIPING RESTRICTION | CHECK INLET HOSE FOR RESTRICTION OR BLOCKAGE |
|  | OIL TOO THICK (OVER 900 SUS @100°F) | CHECK OIL VISCOSITY (MAX: 900 SUS @100°F) |
|  | OIL RUNS TOO COLD-OIL DOESNT' GET OVER 80' F. | CHANGE TO LIGHTER GRADE OF OIL |
| LOW FLOW RATE WITH LOW PRESSURE | AIR BUBBLE IN PUMP | OPEN AIR VENON CANISTER AND THEN, RESTART PUMP |
|  | INSUFFICIENT MOTOR POWER | CHECK FOR PROPER PUMP VOLTAGE AND ROTATION |
|  | OIL BYPASSING THROUGH RELIEF VALVE | CONFIRM THAT RELIEF VALVE IHAS NOT BEEN TAMPERED WITH |
| LOW FLOW RATE WITH HIGH PRESSURE | LOADED FILTER | REPLACE FILTER ELEMENT |
|  | RESTRICTED OUTLET LINES, CLOSED OUTLET VALVE | CHECK AND CLEAR RETURN LINES CONFIRM VALVE IS OPEN |
| EXCESSIVE PRESSURE | RELIEF VALVE SET TOO HIGH | RE-SET RELIEF VALVE TO 75 PSI |
| SHORT FILTER LIFE | EXCESSIVE WATER IN OIL | CHECK SEALS, MAKE SURE COVERS ARE ALL IN PLACE |
|  | EXCESSIVE GLUE IN OIL | CLEAN OUT RESERVOIR, REPLACE SEALS, CHECK GLUE FEED RATE |
| LEAK AT LID CLAMP | CUT OR ERODED SEAL | REPLACE AS NEEDED |
|  | LID NOT TIGHT | TIGHTEN CLAMP BOLT |
| WARNING LIGHT COMES ON BELOW 60 PSI OR ABOVE 75 PSI | PRESSURE SWITCH SET WRONG | RESET PRESSURE SWITCH |
| 01-23-02 |  |  |