HTI Filtration inc.

# SYSTEM SPECIFICATION SHEET

HS220-ENCSS-B4LW-B

System # 810-036A

System Description: Hydra Supreme filtration systems are designed to remove moisture and debris from hydraulic and lubricating oil circuits. The 810-036A model is designed specifically for cleaning Krones labelers with two aggregates. This system comes installed in a stainless steel, water resistant enclosure for use in harsh environment applications. The heart of the systems effectiveness is the patented Hydra Supreme, B4LM series filter that removes both water and glue from the oil. Each system comes complete with stainless steel bulkhead fittings, TEFC motor, pump with safety and monitoring valve train and integrated electrical connector panel.

Physical Data:

Enclosure type:	NEMA 4X construction

Enclosure Height: 	42"  (106 cm)

Width:			36”  (91 cm)

Depth:			12"  (31 cm)

Legs:                           12” (31 cm)

Weight:		 250 lb.  (110 kg)

Material:

Cabinet: 304 Stainless steel, line grain finish

Fluid and electrical fittings: 316 stainless steel

Performance Data:

Pump type: Twin spur gear, fixed external relief

Flow: 1.0 GPM  (oil: 750 SUS @ 100°F @ 50 PSI)

3.8L/min (oil: 108 Cs @ 37.7C @ 3.45 bar)

Water Retention Capacity:  2.00 liter typical

Electrical Specifications:

Motor - 1/2 HP TEFC  50/60 Hz 1 Ph, 3 ph optional

Heater blanket – 2@400 Watts, thermocouple controlled

Timer relay- 36-3600 second adjustable

Electrical Load – 17 FLA

Connection Data:

Oil inlet – 3/4” male 37' JIC

Oil outlet –3/4” male 37' JIC

Electrical Connectors -  DIN 025

810-036A system specification 13002