# HTI FILTRATION INC.

# SYSTEM SPECIFICATION SHEET

# CANFORMING SYSTEMS

# Model # 810-051.1

Systems Description: The 810-051.1 filtration system is designed to remove moisture, sludge and metal particulate from the gear lubricant used in two-piece can manufacturing equipment where 3 phase power is preferred. The filtration system features a sturdy, floor mount stand, close coupled rotary ring gear pump with 3 phase, wash down duty 60 Hz motor and a field adjustable 24 VDC pressure warning light system. This system is designed to provide maximum protection for the bodymaker with absolutely minimal maintenance and service. The heart of the system is the unique, high capacity 400 Series Hydra-Supreme filtration element. This patented filter provides long service life and increases productivity by eliminating the lee jet blocking that affects ram alignment and can body quality . Additional benefits are reduced machine wear and greatly extended lubricant life span through the absorption of coolant and trapping of the fine aluminum particles that abrade the machine surfaces and turn the oil black.

# Physical Data:

# Weight: 42"   (107 c

Width:  13"   (33 cm)

Weight: 113  Lb. (51 kg)

# Material:

# Stand - Powder coated galvanized steel

Canister – Electroless Nickel coated steel

Fittings - Zinc chromate finished, JIC thread

Fasteners - Stainless steel

# Performance Data:

Pump type: Rotary ring gear,  external relief

1.5 GPM  (oil: 750 SUS @ 100°F)

5.7 l/min (oil: 162 Cs @ 40°C)

Oil Quality -  ISO 4406 17-15-13 typical

# Water Retention Capacity: 2.0 liters typical

# Connection Data:

# Oil inlet - 3/4" male 37o JIC

Oil Outlet - 1/2" male 37o JIC

# Electrical Specifications:

# Motor - .50 HP TEFC, Class F Insulation

# 230/460V 60 Hz ,3 Ph

12 Ft.  18-4 SEOOW high voltage cable,

# Pressure Warning System

# Pressure switch - 9.6-32 VDC Field adjustable, PNP  5 m PUR. LED switching and power status

810-051.1 system specification

070312