HTI Filtration inc.

SYSTEM SPECIFICATION SHEET

HF202MR-ENCSS-050-OWB-B

System # 820-010 MR

System Description: Hydro-Fil water removal systems are designed to remove free water and emulsified moisture from hydraulic and lubricating oil circuits. The model 820-010 MR is designed for use in food and beverage packaging areas or harsh environment applications where periodic fluid replenishment is desirable. This system utilizes a pair of the unique, high capacity Hydro-Fil series bag filter to remove large amounts of water from hydrocarbon-based oils.  The HF202 MR model also has a reservoir, which feeds the filter pump on demand to raise the fluid level in the host machine.  This system is designed for gear drive, lubricating and hydraulic fluids ranging from 350 to 900 SUS (at 1000 F). Each system comes complete with dedicated motor, pump with internal relief valve, filter pressure warning light and integrated electrical connector panel.

Physical Data:

Enclosure type:	NEMA 4X construction

Enclosure Height: 	36"  (91 cm)

Width:			30”  (76 cm) 37” (94 CM) WITH REFILL RESERVOIR

Depth:			13"  (33 cm)

Legs:			12”  (31 cm)

Weight:		400 lb. (181 kg)

Material:

Cabinet: 304 Stainless steel, line grain finish

Fluid and electrical fittings: 316 stainless steel

Performance Data:

Pump type: Rotary ring gear, adjustable internal relief

Flow: 1.0 GPM  (oil: 750 SUS @ 100°F @ 50 PSI)

3.8 l/min   (oil: 108 Cs @ 37.7C @ 3.45 bar)

Water Retention Capacity:  2.0 Gal. (7 liter) typical

Electrical Specifications:

Motor - 1/3 HP TEFC  60 Hz  1 Phase

Heater Blanket (2) 400 Watt each

Electrical Requirements - 17 amps-115VAC

Connection Data:

Oil inlet - 3/4” male 37' JIC

Oil outlet - ½” male 37' JIC

Electrical - ½” female NPT (installed on request only)

Electrical Connectors -  DIN 025

Diverter Valve-	  Brass construction with stainless steel ball, Teflon seats

810-020 MR system specification 2-15-02