HTI Filtration Inc.

SYSTEM SPECIFICATION SHEET

System # 830-019

Pneumatic Scale Angelus Part # 1388713

System Description: Hydra Supreme HC211 filtration systems are designed to remove water and particulate from lubricating oil circuits. Our Model 830-019 is designed to work with Angelus seamer systems and is available only through Angelus Sanitary Can. This system applies the patented Hydro-Fil water bag to absorb free and emulsified water in series with the Hydra Supreme series filter element, which removes both hard and soft particulate from the oil supply. The 830-019 is designed for use with lubricating fluids ranging from 350 to 1000 SUS (at 100 F). Each system comes completely assembled and ready for mounting inside the seamer enclosure. This system has a remote mounted motor and pump with internal relief valve, flow sensing switch, dual pressure switches and diversion valve.

Physical Data:

System Height: 	12"  (30.5 cm)

Width:		25”  (63.5 cm)

Depth:		14"  (35.5 cm)

Weight:	              84 lb.  (38 kg)

Material:

Canisters : Electroless nickel coated steel

Frame: Electro polished stainless steel

Performance Data:

Pump type: Rotary ring gear, internal relief

Flow:  0.25 GPM  (oil: 750 SUS @ 100°F)

0.95/min (oil: 108 Cs @ 37.7C)

Safety relief valve set at 90 PSI

Water Retention Capacity:  1.0 liter typical

Electrical Specifications:

Motor - 1/3 HP TEFC  3 phase 50/60Hz 190-460 V

575 V 60Hz also available

Cables: Olflex 150 (Quatro Approval)

Connection Data:

Oil inlet - 1/2" male 37' JIC

Oil outlet - 3/8" male 37' JIC

Safety Switches:

Pressure Switch: AC/DC 5 amp, field adjustable with DIN cable connector

Flow switch - 12-36 VDC voltage, PNP configuration

Filters:

Hydro-Fil 0525 OWB   800-049   Angelus Part # -

Hydra-Supreme B4POPE-   800-050  Angelus Part # -

830-019  system specification  3-1-2012