| TROUBLESHOOTING GUIDE HYDRA-SUPREME MODELS H-210, H-310, H-410 AND H-420 When using this guide please remember that all pressure readings are to be taken with the system at normal operating temperatures. |
| --- |
| SYMPTOM | CAUSE | CORRECTIVE ACTION |
| ERRATIC FLOW RATE, BUBBLES IN OIL STREAM | AIR LEAK IN CONNECTIONS | CHECK FITTINGS FOR TIGHTNESS AND INTEGRITY |
|  | AIR LEAK UNDER RELIEF PUMP ADJUSTMENT NUT | CHECK NUT FOR TIGHTNESS AND GASKET INTEGRITY |
|  | LOOSE OR PINCHED FEED TUBE CONNECTION | MAKE SURE ALL PLUMBING CONNECTIONS ARE TIGHT |
|  | LOW FLUID LEVEL | CHECK FLUID LEVEL IN RESERVOIR |
| EXCESSIVE VACUUM (ABOVE 20" DURING OPERATION) | FLOW RESTRICTION | CHECK ANY INLET STRAINER SCREENS, CLEAN OR BACKFLUSH AS NEEDED |
|  | INLET PIPING RESTRICTION | CONFIRM ½”-3/4" INLET PIPING SIZE |
|  | OIL TOO THICK (OVER 900 SUS @100°F) | CHECK OIL VISCOSITY (MAX: 900 SUS @100°F) |
|  | ENVIRONMENT TOO COLD -LESS THAN 60' FARENHEIT | INSULATE FEED LINE TO FILTER |
|  | OIL RUNS TOO COLD-OIL DOESNT' GET OVER 80' F. | CHANGE TO LIGHTER GRADE OIL |
|  | AMBIENT AIR AND FLUID TEMPERATURE UNDER 60' F. | INSTALL HEAT BLANKET ON FILTER CANISTER |
| LOW FLOW RATE WITH LOW PRESSURE | OIL LEAKING OUT OF SYSTEM | CHECK FOR LEAKS IN PLUMBING |
|  | INSUFFICIENT MOTOR POWER GENERATED | CHECK FOR PROPER PUMP VOLTAGE AND ROTATION |
|  | OIL BYPASSING THROUGH RELIEF VALVE | CHECK RELIEF VALVE FOR PROPER SETTING |
|  | AIR BUBBLE IN PUMP | OPEN BLEED COCK, THEN RESTART PUMP |
|  | RESTRICTED OUTLET LINES | CHECK AND CLEAR RETURN LINES |
| LOW FLOW RATE WITH HIGH PRESSURE | LOADED FILTER | REPLACE FILTER ELEMENT |
| EXCESSIVE PRESSURE | RELIEF VALVE SET TOO HIGH | CHANGE FILTER AND RE-SET RELIEF VALVE TO 65 PSI |
| SHORT FILTER LIFE | EXCESSIVE WATER IN OIL | BLEED OFF WATER IN RESERVOIR |
|  | EXCESSIVE SLUDGE IN OIL | CLEAN OUT RESERVOIR |
| LEAK AT LID CLAMP | CUT OR ERODED SEAL | CHECK SEALS FOR DAMAGE |
|  | LID NOT TIGHT | TIGHTEN CLAMP BOLT |