| TROUBLESHOOTING GUIDE HTI FILTRATION SYSTEM HS410-C2-B6L-C-SPEC.SCM GEAR LUBE FILTER MODEL 810-015 When using this guide please remember that all pressure readings are to be taken with the system at normal operating temperatures. |
| --- |
| SYMPTOM | CAUSE | CORRECTIVE ACTION |
| ERRATIC FLOW RATE, BUBBLES IN OIL STREAM | AIR LEAK IN INLET FITTING | CHECK FITTINGS FOR TIGHTNESS AND INTEGRITY |
|  | CUT OR PINCHED FEED HOSE | VISUALLY CHECK INLET HOSE FOR DEFECTS |
|  | LOW FLUID LEVEL | CHECK FLUID LEVEL IN RESERVOIR |
| EXCESSIVE VACUUM (ABOVE 20") | INLET PIPING RESTRICTION | CHECK INLET HOSE FOR RESTRICTION OR BLOCKAGE |
|  | OIL TOO THICK (OVER 2400 SUS @100°F) | CHECK OIL VISCOSITY (MAX: 00 SUS @100°F) |
|  | OIL RUNS TOO COLD-OIL DOESNT' GET OVER 80' F. | CHANGE TO LIGHTER GRADE OIL |
| LOW FLOW RATE WITH LOW PRESSURE | OIL LEAKING OUT OF SYSTEM | CHECK FOR LEAKS IN PLUMBING |
|  | INSUFFICIENT MOTOR POWER | CHECK FOR PROPER PUMP VOLTAGE AND ROTATION |
|  | OIL BYPASSING THROUGH RELIEF VALVE | CONFIRM THAT CANISTER PRESSURE IS LESS THAN 75 PSI |
| LOW FLOW RATE WITH HIGH PRESSURE | LOADED FILTER | REPLACE FILTER ELEMENT |
|  | RESTRICTED OUTLET LINES | CHECK AND CLEAR RETURN LINES |
| EXCESSIVE PRESSURE | RELIEF VALVE SET TOO HIGH | RE-SET RELIEF VALVE TO 75 PSI |
| SHORT FILTER LIFE | EXCESSIVE WATER IN OIL | BLEED OFF WATER IN RESERVOIR, FIX LEAK |
|  | EXCESSIVE SLUDGE IN OIL | CLEAN OUT RESERVOIR |
| LEAK AT LID CLAMP | CUT OR ERODED SEAL | REPLACE AS NEEDED |
|  | LID NOT TIGHT | TIGHTEN CLAMP BOLT |
| WARNING LIGHT COMES ON BELOW 60 PSI OR ABOVE 75 PSI | PRESSURE SWITCH SET WRONG | RESET PRESSURE SWITCH |