# HTI Filtration Inc.

SYSTEM SPECIFICATION SHEET

HS410-C1-B4H-D

Model # 810-001

Systems Description: The 810-001 filtration system is designed to remove moisture, sludge, varnish and hard particulate from hydraulic fluids to 750 SUS viscosity. The filtration system features a rugged, floor mount stand and comes complete with a dedicated pump, motor and connection fittings. The heart of the system is the unique, high capacity 400 Series Hydra-Supreme filtration element that has proven itself capable of maintaining new oil quality over extended periods of time thus greatly extending the time between periodic fluid replacement, maintaining system accuracy and reducing internal wear.

Physical Data:

Height: 42"   (107 cm)

Width:  13"   (33 cm)

Depth:  18"   (46 cm)

Weight: 90 lb. (41 kg)

Material:

Stand  - Galvanized steel with powdercoat

Canister - Electroless Nickel coated mild steel

Drain valve - Brass

Performance Data:

Pump type: Rotary ring gear, external relief

Flow:  3.0 GPM  (oil: 350 SUS @ 100°F)

11.5 l/min (oil: 650 Cs @ 40°C)

Oil Cleanliness - ISO 4406 16-14-12 typical

Beta3:75

Electrical Specifications:

Motor - 1/2 HP TEFC  WD 60 Hz   1phase

Rotary On/Off Switch

8 Ft. cord with three pronged plug

or 3 phase 60Hz SAE, 50Hz Metric motor

Connection Data:

Oil inlet - 3/4" male 370 JIC

Oil Outlet - 1/2" male 370 JIC

810-001system spec 061812