# HTI Filtration Inc.

SYSTEM SPECIFICATION SHEET

HS410-C1-B4H-C

Model # 810-002

Systems Description: The 810-002 filtration system is designed to remove moisture, sludge, varnish and hard particulate from hydraulic fluids used on servo valve equipped systems. The filtration system features a rugged, floor mount stand and comes complete with a dedicated pump, motor and connection fittings. The heart of the system is the unique, high capacity 400 Series Hydra-Supreme filtration element that has proven itself capable of maintaining better than new oil quality over extended periods of time thus greatly extending the time between periodic fluid replacement, maintaining system accuracy and reducing internal wear.

Physical Data:

Height: 42"   (107 cm)

Width:  13"   (33 cm)

Depth:  18"   (46 cm)

Weight: 90 lb. (41 kg)

Material:

Stand  - Galvanized steel with powdercoat

Canister - Electroless Nickel coated mild steel

Drain valve - Brass

Performance Data:

Pump type: Rotary ring gear, external relief

Flow:  1.5  GPM  (oil: 350 SUS @ 100°F)

5.75 l/min (oil: 650 Cs @ 40°C)

Oil Cleanliness - ISO 4406 14-12-09 typical

Beta3:100

Electrical Specifications:

Motor - 1/2 HP TEFC  WD 60 Hz   1phase

Rotary On/Off Switch

8 Ft. cord with three pronged plug

or 3 phase, 60Hz SAE or 50Hz Metric motor

Connection Data:

Oil inlet - 3/4" male 370 JIC

Oil Outlet - 1/2" male 370 JIC

810-002system spec 061812