# HTI Filtration Inc.

SYSTEM SPECIFICATION SHEET

Model # 810-023, 810-023.1

Systems Description: The 810-023 filtration system is designed to remove sludge and hard particulate from phosphate ester based hydraulic fluids to 500 SUS viscosity. The filtration system features a rugged, wheel mounted stand and comes complete with a dedicated pump, motor, connecting hose and SS drum wands. Model 810-023 is designed for use with general hydraulic systems while the -023.1 system is applied on critical duty systems utilizing servo valves. The system can be used to clear reservoirs, clean oil inside drums and to transfer oil from drums into reservoirs. The heart of the system is the unique, high capacity 400 Series Hydra-Supreme filtration element that has proven itself capable of maintaining new oil quality over extended periods of time thus greatly extending the time between periodic fluid replacement and reducing internal wear.

Physical Data:

Height: 45"   (114 cm)

Width:  24"   (61 cm)

Depth:  16"   (41 cm)

Weight: 155 lb. (74 kg)

Material:

Stand  - Powder coated mild steel

Canister – EN finished steel

Performance Data:

Pump type: Rotary ring gear, internal relief

Flow:  -023 – 3.0 GPM  (oil: 350 SUS @ 100°F)

11.5 l/min (oil: 650 Cs @ 40°C)

Fluid Quality - ISO 4406 13-11-8 typical

-023.1 - 6.0 GPM  (oil: 350 SUS @ 100°F)

23 l/min (oil: 650 Cs @ 40°C)

Fluid Quality - ISO 4406 16-14-12 typical

Electrical Specifications:

Motor - 1/2 HP TEFC  60 Hz   1phase

On/Off Switch at motor junction box

8 Ft. cord with three pronged plug

Connection Data:

Oil inlet - 1" male 37' JIC

Oil Outlet – 3/4" male 37' JIC

810-023system spec 061912