HTI FILTRATION, INC.

SYSTEM SPECIFICATION SHEET

HS410-C2-B6L-C60  	Model # 810-035

HS410-C2-B6L-C50 CE Model # 810-039

Systems Description: The HS410-C2-B6L filtration system, is designed to remove moisture, sludge and metal particulate from the gear lubricant used in two piece can manufacturing equipment. The filtration system features a sturdy, floor mount stand, close coupled rotary ring gear pump and a field adjustable pressure warning light system. The pump and motor are both oversized to compensate for the higher production rates being achieved with the new B-6 Model bodymakers. The model 810-039 uses 3 phase motors and features CE approved components are required. The heart of the system is the unique, high capacity 400 Series Hydra-Supreme filtration element. This patented filter provides long service life and increases productivity by eliminating lee jet blocking, reducing machine wear and greatly extending the effective lubricant life span.

Physical Data:

Height: 42"   (107 cm)

Width:  13"   (33 cm)

Depth:  18"   (46 cm)

Weight: 110  Lb. (50 kg)

Material:

Stand - Powder coated mild steel

Canister – EN coated mild steel

Fittings - Zinc, chromate finished, JIC thread

Fasteners - Stainless steel

Performance Data:

Pump type: Rotary ring gear, adjustable internal

relief and  fixed external relief

Flow:

1.5 GPM  (oil: 750 SUS @ 100°F)

5.75 l/min (oil: 162 Cs @ 40°C)

Water Retention Capacity: 2.0 liters typical

Connection Data:

Oil inlet - 3/4" male 37' JIC

Oil Outlet - 1/2" male 37' JIC

Electrical Specifications:

Motor - .37 KW ,FC , Class F Insulation, Tropicalized, IMB-34, 380-420V/3Ph/50 Hz  (810-039)

12 Ft. 16-4 SOOW power cable  and 12 Ft 18-3 Quattro Approval pressure switch cable

Pressure Warning System

Pressure switch - AC/DC Field adjustable

Warning light - 60 flashes per minute, 50 Candela

810-039 system specification

091802