HTI Filtration inc.

SYSTEM SPECIFICATION SHEET

HF202-ENCSS-050-OWB-B

System # 820-009

System Description: Hydro-Fil water removal systems are designed to remove free water and emulsified moisture from hydraulic and lubricating oil circuits. The 820-009 model is designed for use in food and beverage packaging areas or harsh environment applications This system utilizes the unique, high capacity Hydro-Fil series bag filter to remove large amounts of water from hydrocarbon based oils. The HF202 model is designed for gear drive, lubricating and hydraulic fluids ranging from 350 to 1000 SUS (at 1000 F). Each system comes complete with dedicated motor, pump with internal relief valve, filter pressure warning light and integrated electrical connector panel mounted inside a stainless steel enclosure.

Physical Data:

Enclosure type:	NEMA 4X construction

Enclosure Height: 	36"  (91 cm)

Width:			30”  (76 cm)

Depth:			13"  (33 cm)

Legs:			12”  (31 cm)

Weight:		270 lb. (121 kg)

Material:

Cabinet: 304 Stainless steel, line grain finish

Bulkhead fittings: 316 stainless steel

Performance Data:

Pump type: Rotary ring gear, internal relief

Flow: 1.0 GPM  (oil: 750 SUS @ 100°F)

3.8 l/min   (oil: 108 Cs @ 37.7C)

Water Capacity:  1.5 Gal. (6 liter) typical

Electrical Specifications:

Motor - 1/3 HP TEFC 60 Hz 1 Ph

Heater Blanket (2) 400 Watt each

Connection Data:

Oil inlet - 3/4” male 37' JIC

Oil outlet - ½” male 37' JIC

Electrical - ½” female NPT

Electrical Connectors - DIN 025

Pressure Sensors:

0-160 PSI Adjustable    AC/DC voltage

Warning Light:  110 V- AC 70 Candela Strobe in NEMA4X enclosure

820-009 system specification  wb 010301