HTI Filtration Inc.

SYSTEM SPECIFICATION SHEET

HC211-XP- B4POPE/ 050OWB-A-SPEC.ASCPR4

System # 830-001

Angelus Part # F 029H614

System Description: Hydra Supreme HC211 filtration systems are designed to remove water and particulate from lubricating oil circuits. Our Model 830-001 is designed to work with Angelus seamer systems and is available only through Angelus Sanitary Can. This system applies the patented Hydro-Fil water bag to absorb free and emulsified water in series with the Hydra Supreme series filter element, which removes both hard and soft particulate from the oil supply. The 830-001 is designed for use with lubricating fluids ranging from 350 to 1000 SUS (at 100 F). Each system comes completely assembled and ready for mounting inside an electrical cabinet with the forced lubrication system. Each system has a dedicated motor, pump with internal relief valve, flow sensing switch, dual pressure switches, diversion valve and electrical connection box.

Physical Data:

System Height: 	24"  (61 cm)

Width:		22”  (56 cm)

Depth:		13"  (33 cm)

Weight:	              80 lb.  (36kg)

Material:

Canisters: Electroless Nickel coated mild steel

Pressure Switches: SS body, Lexan lens

Performance Data:

Pump type: Rotary ring gear, internal relief

Flow:  0.5 GPM  (oil: 750 SUS @ 100°F)

1.9l/min (oil: 108 Cs @ 37.7C)

Safety relief valve set at 90 PSI

Water Retention Capacity:  2.0 liter typical

Electrical Specifications:

Motor - 1/3 HP TEFC  1 or 3 phase  190-575 V

Connectors and Rails: DIN EN 50 022, UK 2.5 B

Cables: Olflex 150 (Quatro Approval)

Connection Data:

Oil inlet - 1/2" male 37' JIC

Oil outlet - 3/8" male 37' JIC

Safety Switches:

Pressure Switch: AC/DC 5 amp, field adjustable with DIN cable connector

Flow switch - 12-36 VDC voltage, PNP configuration

Filters:

Hydro-Fil 800-004 -  Angelus Part # -  F029H614 AAI3

Hydra-Supreme 800-016 - Angelus Part # - F029H614 AAJ0

830-001 system specification wb 3-1-99