HTI Filtration Inc.

SYSTEM SPECIFICATION SHEET

HC211- B4POPE/ 050OWB-E-SPEC.ASC M124

System # 830-015        Angelus Part F0007M214 AAAA9

System Description: Hydra Supreme HC211 filtration systems are designed to remove water and particulate from lubricating oil circuits. Our Model 830-015 is designed to work with Angelus seamer systems and is available only through Angelus Sanitary Can. This system applies the patented Hydro-Fil water bag to absorb free and emulsified water in series with the Hydra Supreme series filter element, which removes both hard and soft particulate from the oil supply. The 830-015 is designed for use with lubricating fluids ranging from 350 to 1000 SUS (at 100 F). Each system comes completely assembled and ready for mounting inside the seamer enclosure. This system has a remote mounted motor and dual output pump with external relief valve, (Angelus # F00008M214AAAA7), flow sensing switch, dual pressure switches and low resistance diversion valve for automatic refilling of the Trabon lubricating system.

Physical Data:

System Height: 	24"  (61 cm)

Width:		22”  (56 cm)

Depth:		13"  (33 cm)

Weight:	              84 lb.  (38 kg)

Material:

Canisters: Electroless Nickel coated steel

Frame: Epoxy coated mild steel

Performance Data:

Pump type: Twin spur gear, external relief

Flow:  1.0 GPM  (oil: 750 SUS @ 100°F)

3.8 l/min (oil: 108 Cs @ 37.7C)

Safety relief valve set at 90 PSI

Water Retention Capacity:  2.0 liter typical

Electrical Specifications:

Motor - 1/2 HP TENV Wash Down Duty

3 phase  190-380/415, 208-230/460,575 V

Motor& Pump sold separately as assembly 460-054

Cables: Olflex 150 (Quatro Approval)

Connection Data:

Oil inlet - 1/2" male 37' JIC

Oil outlet - 3/8" male 37' JIC

Safety Switches:

Pressure Switch: AC/DC 5 amp, field adjustable with DIN cable connector

Flow switch - 12-36 VDC voltage, PNP configuration

Filters:

Hydro-Fil 050OWB  800-004 - Angelus Part # -  F029H614 AAI3

Hydra-Supreme B4POPE- 800-016 -Angelus Part # - F029H614 AAJ0

Spin on filter Water Resistant  800-042

830-015 system specification wb 4-03-00