OPERATORS MANUAL

HYDRA-CLEAN FLUID SCRUBBING SYSTEM

HC211

## 830-022.1

INTRODUCTION:

Hydra-Clean fluid scrubbing systems are high performance industrial filters designed to remove particulate and water from hydraulic and lubricating oil systems.  Manufactured from durable, corrosion resistant materials, they are designed for constant, uninterrupted use without immediate supervision. The Hydra-Clean HC211 system utilizes two elements in series to remove water, and then particulate from the working fluid.  This system ensures a high degree of fluid purity with an absolute minimum of maintenance and service requirements.

This operating manual is designed to provide you with the basic information to economically and efficiently service your fluid scrubbing system.  HTI welcomes your comments and our technical service staff is available to assist you in applying our equipment to solve your fluid purity problems.

SYSTEM OPERATION:

The Hydra-Supreme HC211 filtration system uses two separate filtration elements in series to progressively clean the working fluid.  Fluid is drawn from the reservoir up through a check valve by a rotary pump.  Where space requires that the filtration unit be set up farther than 10 feet (3 meters) from the reservoir a booster pump may be required. If the vacuum gauge reads in excess of 20" a booster pump is recommended. The fluid is then pushed through the flow sensing and pressure switch assembly into the water removal bag element where the free and emulsified moisture is absorbed.  The partially cleaned solution then passes through the axial flow  media filter where both soft and hard particulate contamination is removed. The filtered oil then passes through a set of solenoid operated selector valves and back into either the pressurized lubrication system, the upper turret or base reservoir.  If the contamination level in the oil is high, or if the filters are nearing capacity, several passes through the system may be required for total cleansing of the oil.

The check valve ensures adequate oil supply to wet the pump during start-up and prevents drain back when the system is shut-off. The vacuum gauge indicates the resistance to flow and has a manual bleed cock that should be cracked open for safety relief during initial start-up in case the motor is rotating backwards.  Typical vacuum readings are from 3 - 10 “ (The bleed cock on the outlet elbow of the pump is to relieve entrapped air from the pump chamber so that oil can be drawn in to restore pump suction.

An internal relief valve that is factory set at 70-PSI controls pump output pressure. We do not recommend changing this setting. Removing the acorn nut covering the adjustment screw without proper tools can result in an intake air leak that will require a new gasket.

The pump output and service life of the two filter elements are monitored by a series of flow and pressure switches.  The flow switch monitors the volume of oil being pumped

through the system. It is used to indicate when flow through the system has dropped below the minimum level required for adequate oil cleansing and replenishment of the  lubrication pump reservoir.  A flow failure is indicated by the red "no oil flow" light on the main panel and the illumination of the indicator lamp inside the flow switch. The flow switch is factory set at .22-.25 GPM (.83 -.95 l/min) and field adjustment is not advised. A pair of stepped pressure switches monitors the system pressure. The initial switch indicates that a filter change-out will be required soon.  The second pressure switch indicates that the filter needs to be changed promptly.  Pressure switch settings are field adjustable and must be set to reflect the type of oil used and operating temperatures the filter is working with to receive maximum use from the filters. The initial (left hand) switch typically activates at 10 PSI (.66 BAR) above the start-up pressure and secondary (right hand) switch at 12-14 PSI (.9-1.0 BAR). Because each installation and packaging operation is different  it is important that the pressure switches be set in the field. Complete field adjustment instructions are included in this manual.

The selector valves are operated by remote sensing switches and timers, which vary depending on which options are selected at the time of order.  The maximum line resistance pressure on the diverter valve should be less than 20 PSI (1.20 Bar) when the valve is activated.

SYSTEM PRESSURES:

Pressure readings will vary widely with the oil viscosity, ambient air temperature and temperature of the oil entering the filtration system.  It is also not unusual for system pressures to rise substantially over normal levels when re-starting a system that has been left off for several days or when changing particulate filters. Typically the system will return to normal levels after 45-60 minutes as the warm oil from the seamer flushes out the cooler oil from the filter elements and the filtration passages in the new element open under pressure. A timed delay in the pressure switch alarms should be programmed in for these reasons.  In cold climates it may be necessary to heat the Hydra-Supreme axial filter canister to maintain the desired 80-85°F operating temperature.

Factory Set Warning Pressures and Change Out Pressures

Using 750 SUS (150 ISO) lubricant @ 100°F

Warning Switch - 28 PSI / 2 BAR  Change Filter Switch - 33 PSI / 2.3 BAR

Typical bag element change out is 08 -10 PSI ( .55- .70 BAR) increase over new element pressure.  All measurements should be made when system is fully warmed to operating pressure.

OIL SELECTION INFORMATION:

HTI Filtration has tested many oils commonly used in seamers. While we do not recommend a specific brand or type of oil we do recommend that you use a high quality oil that has good hydrolytic stability. That is, an oil that can be exposed to water repeatedly and dried without deleting or precipitating the additive package.

The viscosity of the oil plays a major role in determining the operating pressure of the system. A 40 Wt. oil rated at 750 SUS at 100°F is actually 2,000 SUS at 75° F, a 260% increase in viscosity!  Even small temperature changes can result in significant pressure variations in the system.  It is not uncommon for a cold filter system to read higher pressures in the morning and then have them drop off as the system components warm over several hours to an even operating temperature.

Field Adjustment of Pressure Switches

Before changing any settings on a Hydra-Clean Fluid Conditioning System run the seamer and filter until the oil is at the normal operating temperature (typically between 75-100°F). This normally takes several hours because of the relatively low flow volume and high metal mass of the components.

NOTE: Do not attempt to reduce or increase the operating pressure by adjusting the internal pressure relief valve on the pump. This safety devise has been set and locked into place at the factory. Attempting to adjust the pressure setting screw can jam the relief valve and prevent proper movement. Improperly removing the acorn nut may also result in air leaking into the system, which will require 	frequent system bleeding until the acorn nut seal is replaced.

1.	Turn filter system on and allow oil to fill both canisters while venting the air through the bleed cocks on the canister lids.

2.	As soon as fluid flows from bleed cock, close and secure.

3.	Allow filter system to run for 60-120 minutes to flush cold oil out of the filters and bring entire system up to operating temperature. Note the operating pressures of the filters.

4.	Slowly close the 1/4" ball valve at the base of the Hydra-Supreme (left hand side) canister until the system pressure is 10-12 PSI higher than the reading in Step 3.

5.	Remove cover of warning pressure switch (right hand switch) and adjust it 			by rotating the SET ring until LED illuminates. The RESET ring should be 			set 5 PSI below the level of the SET ring. Place the cover back on the 			switch

6.	Increase system pressure by 5 PSI by further closing the valve and then adjust the maximum pressure switch (left-hand switch) the same way as in Step 5.

7.	Open the ball valve to relieve the pressure build-up and allow the system to run for 10-15 minutes before recording the pressures for future reference.

SYSTEM LOCATION:

Although the Hydra-Clean system uses a self-priming pump it is advisable to keep the filter below, and as close to the reservoir as possible.  A suction line vacuum condition no greater than 20"hg should be experienced during start-up or normal operation.  Pump damage will occur at vacuum levels above 24” hg. Where pump suction is high either larger inlet pipe size or a booster pump is required. We recommend using the HTI booster pump system 460-064 as it is pre-set for proper boost pressure and maximum efficiency.

Remote mounted filters will also experience higher-pressure readings due to the increased return line resistance.

Set the filtration system cabinet on a solid, level surface.  Allow a minimum of 24" of frontal clearance for service access.  Locate filter away from sources of moisture and heat, filter system must be kept below 140°F, and be protected from moisture.

PLUMBING:

Inlet tubing should be 3/4"- 1” with a preferred maximum distance of 20’.  Smaller tubing can be utilized where the connection runs are shorter and/or the operating temperature is above 80° F.

The solenoid ports utilize 1/2” JIC fittings; flow selection is determined by remote activation of the solenoid valve from the main control panel.  Outlet lines to the main reservoir and lubricating system should be  minimum of 3/8"  with 1/2" or larger  preferred.. Ball valves can be installed at both reservoir connections for easy shut off during installation or service.

ELECTRICAL:

The motor utilizes 3 phase, 50/60 Hz power with a number of voltage options. Please check the nameplate on your motor if you are unsure of your power type.

The pressure switches, solenoid coils and flow sensor come standard using 24 VDC operating power.  120 VAC  power is optional for all the sensors .

The power source for the filter should be independent of the basic machine control, as the oil filtration system should run continuously for efficient contaminant control.

INITIAL START-UP PROCEDURE

Upon completion of the electrical and hydraulic connections the Hydra-Clean system is ready for start-up.  The HC211 is factory adjusted to perform with a fluid viscosity of 750 SUS (164 C ST at 40°C) at 100°F.  To use different viscosity fluids or to run at

different temperatures please make the recommended changes to the switch settings.  See the previous section in this manual for further information on adjusting the pressure settings.

FILTER SYSTEM START-UP:

Crack open the petcock between the check valve and the pump inlet. Turn the electrical power on to start the gear pump.  Make sure the inlet and return lines to the reservoir are free of restriction and all valves are open.  Crack open the bleed cocks at the top of both canisters.  As soon as fluid starts to flow from the bleed hole close the cock securely and wipe the fluid from the canister top.  Let the system warm up to typical operating temperature.

When initially starting the Hydra-Clean system air may enter the plumbing lines in sufficient quantity to keep the pump from priming itself or create a false reading in the oil flow sensor.  Should this occur you must bleed off this trapped air by opening the bleed cock located at the pump outlet elbow just above the union.

NOTE:	Your Hydra-Clean fluid scrubbing system should have no occasion to exceed 95 PSI when properly installed and using the recommended type fluid.  Should a pressure condition exceed the recommended maximum immediately shut off the filtering system and contact HTI  for assistance.

FILTER ELEMENT REPLACEMENT

BAG ELEMENT:HYDRA-FIL

A new bag element should be installed after the system has been in service for a  maximum of  6 months or shows an 8-10 PSI pressure increases.

Step 1:	Turn off the Filter System.  It is not necessary to turn off the seamer to service the filter.

Step 2:	Open the drain cock at the bottom of the bag (left hand) canister then open the bleed cock at the top.  The 3/8" hose can be used to direct the oil to a container where it can be poured back into the canister for re-use.

Step 3:	When canister is empty remove the canister clamp ring and lift off the lid.

Step 4:	Examine the "O" ring for wear, replace this ring if it shows signs of wear or if the canister was leaking.

Step 5:	Slowly lift the bag out by the strap allowing the captured oil to drain back into the canister.  Hang the bag over a receptacle if you want to reclaim the approximately 3 cups of oil entrained in the bag.

Step 6:	Slice open the plastic bag holding the new bag.  Carefully remove the bag and straighten to its full length.  Slide the new bag into the colander using the fabric strap to push the metal bag ring down firmly onto the seat.  Do not use the fabric strips inside the bag to seat the filter, they will tear off.

Step 7:	Close the drain cock and fill the bag with the drained oil captured in Step 2.

Step 8:	Put the "O" ring back on the canister lip, replace the lid, clamp and tighten.

Step 9:	Start the motor and allow the air to escape through the bleed cock.  Close the cock when fluid starts to come out, wipe off the unit and check for leaks.

AXIAL ELEMENT: HYDRA SUPREME

Step 1:	Turn off the Filter System.  It is not necessary to turn off the machine being protected to service the Hydra-Supreme filter.

Step 2:	Open the drain cock on the bottom of the canister, then open the bleed cock on the top of the canister.  The 3/8" ID hose can be used to direct the draining oil to a receptacle.  Drained oil can later be used to refill the canister.

Step 3:	Remove the canister clamp ring and lift off the canister lid.

Step 4:	Examine the canister "O" ring for cracks and wear spots.  If the canister lid seal was leaking, or if the "O" ring shows signs of wear, replace the ring.

Step 5:	Unscrew the "T" handle (CCW motion) assembly that holds the filter in place.  The cup seal on the handle assembly should be smooth and free of rough spots or tears.  Replacement seals are available.

Step 6:	Slice open the end of the plastic bag holding the new element.  Remove the new element and set in a clean area.  Lift used element off of center post and slide it into plastic bag.

Step 7:	Slide new element over the center post.  Make sure the pull strap is at the top.  Insert "T handle" into top of element and turn in a  CW motion until the handle firmly stops.

Step 8:	Close drain cock and refill canister with oil.

Step 9:	Put the "O" ring back on the canister lip, replace lid, clamp and tighten.

Step 10:	Start the pump motor and allow air to bleed out through bleed cock on top of canister.  Close bleed cock when fluid starts to come out.  Wipe off unit and check for leaks.

CAUTION

Some hydrocarbon oils are not suitable for extended use after they have been mixed with water.  These non-hydrolytically stable lubricants tend to precipitate out their additives, which are captured by the Hydra-Supreme axial filter element.  These oils look acceptable but no longer have the original anti-wear and anti-oxidization characteristics of new oil.

HTI Filtration recommends that you use a premium grade lubricant whenever you have an on-going water contamination problem and that you consult your lubricant supplier for specific information on your specified oil

.