TROUBLESHOOTING GUIDE

HTI FILTRATION SYSTEM HF202-ENCSS-050-OWB-B

MODEL 820-010 “CAMEL”

When using this guide please remember that all pressure and flow readings are to be taken with the system at normal operating temperatures.

| SYMPTOM | CAUSE | CORRECTIVE ACTION |
| --- | --- | --- |

ERRATIC FLOW RATE,

| BUBBLES IN OIL STREAM | CUT OR PINCHED HOSE | VISUALLY CONFIRM HOSE INTEGRITY |
| --- | --- | --- |
|  | AIR LEAK UNDER RELIEF PUMP ADJUSTMENT NUT |

CHECK NUT FOR TIGHTNESS

| AND GASKET INTEGRITY |
| --- |
|  | LOOSE HOSE CONNECTION |

MAKE SURE ALL PLUMBING

| CONNECTIONS ARE TIGHT |
| --- |
|  | LOW FLUID LEVEL |

CHECK FLUID LEVEL IN

RESERVOIR

EXCESSIVE VACUUM

| (ABOVE 20") | FLOW RESTRICTION | CHECK INLET LINES AND VALVES |
| --- | --- | --- |
|  | INLET PIPING RESTRICTION |

CONFIRM  ¾-1" INLET PIPING

SIZE

OIL TOO THICK

(OVER 900 SUS @100°F)

CHECK OIL VISCOSITY

| (MAX: 900 SUS @100°F) |
| --- |
|  | ENVIRONMENT TOO COLD -LESS THAN 60' FARENHEIT |

INSULATE FEED LINE TO

| FILTER, HEAT CANISTERS |
| --- |
|  | OIL RUNS TOO COLD-OIL DOESNT' GET OVER 80' F. |

CHANGE TO LIGHTER

| GRADE OIL, HEAT CANISTERS |
| --- |
|  | AMBIENT AIR AND MACHINE TEMPERATURE UNDER 60' F. |

INSTALL HEAT BLANKET ON

FILTER CANISTER

LOW FLOW RATE WITH

| LOW PRESSURE | RELIEEF VALVE SET TOO LOW | TIGHTEN SPRING IN RELIEF PUMP |
| --- | --- | --- |
|  | INSUFFICIENT MOTOR POWER GENERATED |

CHECK FOR PROPER PUMP

| VOLTAGE AND ROTATION |
| --- |
|  | AIR BUBBLE IN PUMP | BLEED AIR |

LOW FLOW RATE WITH

| HIGH PRESSURE | LOADED FILTER | REPLACE FILTER ELEMENT |
| --- | --- | --- |
| SYMPTOM | CAUSE | CORRECTIVE ACTION |
|  | RESTRICTED OUTLET LINES |

CHECK AND CLEAR RETURN

LINES

EXCESSIVE PRESSURE

RELIEF VALVE SET TOO

| HIGH | CHANGE FILTER AND RE-SET RELIEF VALVE TO 65 PSI MAX |
| --- | --- |

PUMP WON'T WORK AFTER

| ELEMENT CHANGE | VACUUM LOCK IN PUMP |
| --- | --- |

BLEED AIR OFF AT BLEED

| VALVE ON PUMP OUTLET |
| --- |
| REMOTE RESERVOIR WON'T REFILL GEAR BOX | FAULTY SOLENOID COIL |

CHECK COIL ON SOLENOID,

| REPLACE IF DEFECTIVE |
| --- |
|  | LEVEL CONTROLS TURNED OFF | CHECK POWER TO CONTROLS |

CANISTERS LEAK AT LID

| CLAMP | CUT OR ERODED SEAL | CHECK SEALS FOR DAMAGE |
| --- | --- | --- |
|  | LID NOT TIGHT | TIGHTEN CLAMP BOLT |

WARNING LIGHT SEQUENCE:

RED LIGHT – CHANGE WATER ABSORPTION BAGS

YELLOW LIGHT – REFILL REMOTE RESERVOIR

TSG820-010

05-10-00