| TROUBLESHOOTING GUIDE ANGELUS SANITARY CAN SEAMER FILTRATION SYSTEM HYDRA-SUPREME MODEL H-211-ASC R3-R6 When using this guide please remember that all pressure and flow readings are to be taken with the system at normal operating temperatures. |
| --- |
| SYMPTOM | CAUSE | CORRECTIVE ACTION |
| ERRATIC FLOW RATE, BUBBLES IN OIL STREAM | AIR LEAK IN FITTINGS, BLEED COCK OR VACUUM GAUGE | CONFIRM THAT VACUUM BLEED AND GAUGE ARE AIR TIGHT, CHECK FITTINGS |
|  | AIR LEAK UNDER RELIEF PUMP ADJUSTMENT NUT | MAKE SURE TORQUE STRIPE ON ACORN NUT IS INTACT, REPLACE SEAL IF BROKEN |
|  | LOOSE OR PINCHED FEED TUBE CONNECTION | MAKE SURE ALL PLUMBING CONNECTIONS ARE TIGHT |
|  | LOW FLUID LEVEL | CHECK FLUID LEVEL IN RESERVOIR |
| EXCESSIVE VACUUM (ABOVE 15") | FLOW RESTRICTION | CHECK INLET PIPING FOR RESTRICTION, BLOCKAGE |
|  | INLET PIPING RESTRICTION | CONFIRM ¾”-1" INLET PIPING SIZE |
|  | OIL TOO THICK (OVER 900 SUS @100F) | CHANGE TO LIGHTER GRADE OF OIL |
|  | ENVIRONMENT TOO COLD -LESS THAN 60' FARENHEIT | INSULATE FEED LINE TO FILTER, HEAT CANISTERS |
|  | SEAMER RUNS TOO COLD-OIL DOESNT' GET OVER 80' F. | CHANGE TO LIGHTER GRADE OIL |
|  | AMBIENT AIR AND SEAMER TEMPERATURE UNDER 80' F. | INSTALL HEAT BLANKET ON FILTER CANISTER |
| LOW FLOW RATE WITH LOW PRESSURE | AIR BUBBLE IN PUMP | OPEN AIR VENTS TO BLEED OF AIR |
|  | INSUFFICIENT MOTOR POWER GENERATED | CHECK FOR PROPER PUMP VOLTAGE AND ROTATION |
|  | OIL BYPASSING THROUGH RELIEF VALVE | CHECK RELIEF VALVE FOR PROPER SETTING |
| SYMPTOM | CAUSE | CORRECTIVE ACTION |
| LOW FLOW RATE WITH HIGH PRESSURE | LOADED FILTER | REPLACE FILTER ELEMENT |
|  | RESTRICTED OUTLET LINES | CHECK AND CLEAR RETURN LINES |
| EXCESSIVE PRESSURE | RELIEF VALVE SET TOO HIGH | CHANGE FILTER AND RE-SET RELIEF VALVE TO 65 PSI |
| PUMP WON'T WORK AFTER ELEMENT CHANGE OR STRAINER CLEANING | VACUUM LOCK IN PUMP | BLEED AIR OFF AT BLEED VALVE ON PUMP OUTLET |
| UPPER TURRET OR LUBRICATOR WON'T FILL | FAULTY SOLENOID COIL | CHECK COIL ON SOLENOID, REPLACE IF DEFECTIVE |
| CANISTERS LEAK AT LID CLAMP | CUT OR ERODED SEAL | CHECK SEALS FOR DAMAGE |
|  | LID NOT TIGHT | TIGHTEN CLAMP BOLT |